Safety Test from Automotive Service

Choose your answers to the Safety Test from this list:

1½

6

air

air

asbestos

B

back, eyes

belt

blowguns

charger

data sheet

disconnected

drill

drilling

electrical

end

explosions

eye or face

fire

flash

freeze

gasoline

gravity

green

grinders

ground

handle

hydraulic

hydraulic jack

impact

instructor

jack

jack

legs

manual

reground

rest

side

spontaneous

squeezing

talk

vapor

water

water

water

wrench

1. If you should become injured while working in the shop, inform your ___________ immediately.

2. The most common injuries in an automotive shop involve the ___________ and ____________.

3. Lift with your _________________, not your back.

4. If a ______________ is burning out of control, leave the area immediately and call for help.

5. A flammable liquid fire is called a Class ____ fire.

6. Keep oily materials separated from air to prevent ______________________ combustion.

7. What form of gasoline is the most dangerous, liquid or vapor (circle one)?

8. Never use _____________ to clean floors or parts.

9. The temperature at which a flammable liquid’s vapors will ignite when brought into contact with an open flame is called the _________ point.

10. Disconnect the battery _______________ cable before working on a vehicle electric system.

11. Before an ____________ fire can be extinguished, the battery must be disconnected.

12. Do not attempt to put out a gasoline fire with _________________.

13. The information sheet about a hazardous material is called a material safety ____________________________ (MSDS).

14. If caustic Alkaline liquid (from the hot tank) gets into your eyes flush with _________________, especially under the eyelids.

15. A HEPA vacuum is a special vacuum for ___________________.

16. The color of the wiring for ground on commercial and household electrical wiring is ____________________________.

17. Electric cooling fans should be ________________ before working around them.

18. Before opening a radiator, test for pressure in the system by ______________ the top radiator hose.

19. Mushroomed punches or chisels should be _________________________ before use.

20. Always wear ___________________ protection when using hammers, chisels, pullers, batteries,

air-conditioning machinery, compressed air, and other hazardous situations.

21. Always use a ________________ on the tang of a file.

22. Compressed __________________ can penetrate skin and must be used cautiously.

23. Do not ___________________ to someone who is operating a machine.

24. A ___________ bit has a tendency to grab the work when it just begins to break through the metal.

25. When _________________ sheet metal or large pieces of metal on the drill press, make sure they are clamped to the work table.

26. Stand to the ________________ when starting the grinder.

27. Position the tool ___________________ as close to the grinding wheel as possible.

28. Rubber-tipped __________________ work at full shop air pressure.

29. When using an air impact wrench, be sure to use an extra thick socket, called an __________ socket.

30. When an air impact __________________ is used with a wobble socket, the socket can fly off if the tool is started when the socket is not on the bolt head.

31. Die _____________________ turn at speeds of up to 20,000 rpm. Be sure to use wheels that are rated for that high a speed.

32. Because they can develop force of from 20–50 tons, _______________ presses can cause parts to explode.

33. Locate the correct lift points in the service ______________________ before using a hydraulic service jack or lift.

34. When lifting a vehicle on a frame-contact lift, place the lift adapters at the specified locations and raise the vehicle about __________”. Then, shake it to see that it is firmly placed.

35. Use a ______________ _______________ to raise and lower a vehicle only.

36. A jacked-up vehicle should be placed firmly on _____________________ stands.

37. When moving an engine that is mounted on a shop crane, be sure the engine is lowered as far as possible to keep the center of __________ low.

38. Bolts that attach an engine sling or engine stand adapter to the block should enter the block at least ___________ turns.

39. When using a transmission _______________ on a car that is on a frame-contact lift, be careful not to raise the car off the lift adapters as you raise the transmission.

40. The most common cause of battery ____________ is when someone unhooks the battery charger without turning it off.

41. Shut off and unplug the battery ________ before unhooking either of the cables.

42. If acid gets on the skin or eyes, immediately flush with _____________ for at least 15 minutes.

43. If refrigerant from an air conditioning system contacts your skin or eyes it will _____________ them.

44. The keys should be out of the ignition any time a ______________ is being inspected or adjusted.

45. When a floor creeper is not in use, it should be stood on ___________________ so it is not accidentally stepped on.

46. Be careful around hybrid vehicle wiring that is colored ____________.